## Slide 1: CT
Jonathan Disselhorst, PhD
Jonathan.Disselhorst@med.uni-tuebingen.de

## Slide 2: Overview
X-rays and interaction
Detectors and scanners

## Slide 3
X-Ray Production

## Slide 4: Production of X-Rays
Bushberg et al. The Essential Physics of Medical Imaging
Spanish National Research Council [CSIC] (http://www.xtal.iqfr.csic.es/)

## Slide 5: Production of X-Rays
Bremsstrahlung
Characteristic Radiation
Bushberg et al. The Essential Physics of Medical Imaging

## Slide 6: X-Ray Spectrum
Filtered Bremsstrahlung
Spectrum
Characteristic
Radiation Spikes
(Tungsten)
Adapted from Bushberg et al. The Essential Physics of Medical Imaging
Unfiltered
Bremsstrahlung
Maximal Photon
Energy (90 keV)

## Slide 7: X-Ray Spectrum: Different kVp
Bushberg et al. The Essential Physics of Medical Imaging
kVp:
Peak Tube Voltage [kilo-Volts]
mAs:
Tube current [milli-Ampere]
multiplied by
Exposure time [seconds]

## Slide 8: X-Ray Spectrum: Different mAs
kVp:
Peak Tube Voltage [kilo-Volts]
mAs:
Tube current [milli-Ampere]
multiplied by
Exposure time [seconds]
Bushberg et al. The Essential Physics of Medical Imaging

## Slide 9: X-Ray Spectrum: Filtering
kVp:
Peak Tube Voltage [kilo-Volts]
mAs:
Tube current [milli-Ampere]
multiplied by
Exposure time [seconds]
Bushberg et al. The Essential Physics of Medical Imaging
“Beam Hardening”

## Slide 10: Current
Tube current ≠ Filament current
Tube voltage ≠ Filament voltage
Bushberg et al. The Essential Physics of Medical Imaging
Spanish National Research Council [CSIC] (http://www.xtal.iqfr.csic.es/)
Notes: The tube voltage is around 80 kilovolt, the filament voltage is approximately 10V
The tube current depends on the filament current, but also on the tube voltage

## Slide 11
X-Ray Interaction

## Slide 12: Rayleigh Scattering
Bushberg et al. The Essential Physics of Medical Imaging
Dominant form of elastic scattering of X-rays in medical imaging.
At low energies.

## Slide 13: Compton Scattering
Bushberg et al. The Essential Physics of Medical Imaging
Dominant interaction in soft tissue in medical imaging.
Inelastic scattering.

## Slide 14: Photoelectric Effect
Bushberg et al. The Essential Physics of Medical Imaging
Instead of characteristic X-rays (shown here), Auger electrons could be emitted (not shown).
The probability of characteristic X-rays decreases with lower atomic number (Z). The probability is not very high in tissue (Zeff = 7).
Can occur when the energy of the photon ≥ binding energy of the electron

## Slide 15: Attenuation
The Mass Attenuation Coefficient is independent of density

## Slide 16: Photoelectric Effect
Bushberg et al. The Essential Physics of Medical Imaging
J Am Coll Cardiol Img. 2015;8(6):710-723. doi:10.1016/j.jcmg.2015.03.005

## Slide 17: Mass Attenuation Coefficients
Adapted from Bushberg et al. The Essential Physics of Medical Imaging
Radiology ~20-80 keV
Nuclear Medicine ~80-511 keV

## Slide 18: Attenuation in Tissue
Data from the US National Institute of Standards and Technology (NIST)
http://physics.nist.gov/PhysRefData/XrayMassCoef
K-edge (33 keV)

## Slide 19
X-Ray Detection

## Slide 20: Detector

## Slide 21: Fan- / Cone beam
Bushberg et al. The Essential Physics of Medical Imaging

## Slide 22: Siemens Inveon CT
Source
Detector

## Slide 23: Hounsfield Units
Distilled water at standard pressure and temperature is defined as 0 HU
Air is defined as −1000 HU
In a voxel with average linear attenuation coefficient μ, the HU value is:
Godfrey Hounsfield

## Slide 24: Typical HUs
Substance | HU
Air | −1000
Lung | −500
Fat | −100 to −50
Water | 0
CSF | 15
Kidney | 30
Blood | +30 to +45
Muscle | +10 to +40
Grey matter | +37 to +45
White matter | +20 to +30
Liver | +40 to +60
Soft Tissue, Contrast | +100 to +300
Bone | +700 (cancellous bone) to +3000 (cortical bone)