## Slide 1
Cross sectional anatomy:
Thorax / Abdomen
Dr. Mareen Kraus
Departement for diagnostic and interventional radiology
Clinical director: Prof. Dr. Konstantin Nikolaou
I-Klic I

## Slide 2: Learning points
technical basics of cross sectional imaging
Basic anatomy of the thorax and abdomen for use in cross sectional imaging
Examples of thoracic and abdominal CT pathology
Notes: Maaz, Horst 13.4.26

## Slide 3
What are the possible techniques for cross sectional imaging?

## Slide 4: Computertomography (CT)
aus: Krug, Thoraxdiagnostik, Thieme 2004
Siemens Healthcare
Body is examined by the use of rotating X-ray tubes

## Slide 5: Magnetic Resonance Imaging (MRI)
Imaging based on strong magnetic fields
Siemens Healthcare

## Slide 6: What dos CT mean for the cross sectional imaging?
Used to answer most clincal questions:
Emergency radiology (quick imaging of the whole body)
Oncology
Pulmonary lung changes
MRI used for specific questions regarding organs:
Heart imaging
Liver imaging
Billiary duct imaging
By absolute contraindication for CT (e.g. strong allergeic CM reaction)

## Slide 7
Thorax-CT
Start approx. 2 cm above the sternal notch to diaphragm
Spiral-CT-technique in caudocranial or craniocaudal direction
Slice thickness 3(-5) mm
Deep inspiration with raised arms lying on the back
duration: < 10 sec
Topogramm (syn. Scout view)
Scan Protocol
Notes: Die von der Röntgenröhre abgegebene Strahlung beinhaltet ein Spektrum mit hohen und niedrigen Energien. Mit zunehmender Dicke des durchstrahlten Objekts werden die niederenergetischen Anteile stärker absorbiert als die höherenergetischen („Strahlungsaufhärtung“). Für die Zuordnung der CT-Werte muss die Absorption für Wasser bei einer bestimmten „mittleren“ Energie angenommen werden. Da bei höheren Energien die Absorption zurückgeht, würden die CT-Werte mit zunehmender Aufhärtung absinken. Technisch wird dieses Problem dadurch gelöst, dass man aus der Strahlungsabsorption für jede Einzelprojektion auf die Dicke des durchstrahlten Objekts rückschließt und die entstehende Strahlungsaufhärtung rechnerisch korrigiert. Diese rechnerische Korrektur setzt voraus, dass das gesamte Objekt aus nur einer Substanz (üblicherweise Wasser) besteht. Weicht die atomare Zusammensetzung lokal deutlich von Wasser ab (Knochen, Metalle, jodhaltiges Kontrastmittel), so treten weiterhin Aufhärtungsartefakte auf.
Neuere Verfahren erlauben eine zunehmende Reduktion der Aufhärtungsartefakte. Dies gelingt entweder durch aufwändige Rechenalgorithmen, die aus der Dichteverteilung im CT-Bild auf die lokale Aufhärtung rückschließen (z. B. RASP bei Toshiba), oder durch den Einsatz dünnerer Schichten, die zu größeren Schichtdicken zusammengesetzt werden (auf diese Weise lässt sich die Aufhärtung von schräg durch die Schicht verlaufenden Strukturen herabsetzen).

## Slide 8
Scan Protocol
Scan-Area: diaphragm to iscial tuberosity
Slice thickness 3-5 mm
inspiration with raised arms lying on back
NB: radiation exposure
10-20 mSv! Depending on scanner type, patient constitution, scan settings, etc.
If required oral contrast (water, iodine CM)
Abdomen-CT
Topogramm (syn. Scout view)

## Slide 9: Contrast Media (CM)
Oral and rectal:
  water soluble, iodine: Amidotrizoat (Gastrografin©)
  (positive CM)  suspiscion of perforation, abscess, fistula
  Water / Mannitol (negative CM)  investigation of gastric/intestinal wall, e.g. tumor, inflammation, ischaemia
Intravenous (i.v.):
  CT-angiography (vascular imaging)
  vascular identification (to differentiate from lymph nodes)
  interstitial CM-take up (inflammation and tumor diagnosis)
  Anionic, low molarity iodine CM = today‘s standard
Which possible ways of utilising contrast media are there?

## Slide 10: What does intravenous contrast media look like?
nativ
nach Prokop et al.
Contrast Media

## Slide 11: What does intravenous contrast media look like?
nativ
nach Prokop et al.
Contrast Media
Normal or contrast enhanced ?
Which body region?
CT or MRI ?

## Slide 12: What does intravenous contrast media look like?
nativ
Kontrast-angehoben
nach Prokop et al.
Contrast Media

## Slide 13
Phases of the Contrast Media
Upper abdomen - no contrast
arterial – approx 20 s after start of injection
Portal vein –. 60-90 s after start of injection
Urological phase – 5-15 min after start of injection
-foreign material
-plaques
-haematoma
-arteries
-hypervascular lesions
-parenchymal lesions
-portal vein
-drainage
Injection in cubital vein, speed of flow mostly
2-3 ml/s by pump
Quelle: Medrad Bayer Healthcare

## Slide 14
The depth of grey scaling within a CT ranges from -1000 to +3000, however the human eye can only differentiate between 30 - 40 greyscales.
→ The window settings must therefore be appropriate for the structures being analysed.
1500 / -500
350 / 50
2000 / 200
Soft tissue -window
Pulmonary-window
bone-window
Window Settings
Window width W / window central C

## Slide 15: Slicing
Conventional view is from the foot of the patient
→ the left side of the image is the patient‘s right
R
L
Thieme Radbase

## Slide 16
Anatomy of the Thorax

## Slide 17
Ascending Aorta
Descending Aorta
Pulmonary trunk
Left pulmonary artery
Main bronchi
Carina

## Slide 21
Pulmonary trunk
Right pulmonary
artery

## Slide 22
Left Ventricle
Right Ventricle
Vena cava inferior
Right Atrium

## Slide 25
Anatomy of the Abdomen

## Slide 26
„Normal Anatomy“

## Slide 27
„Normal Anatomy“

## Slide 28
„Normal Anatomy“

## Slide 29
„Normal Anatomy“

## Slide 30
„Normal Anatomy“

## Slide 31
„Normal Anatomy“

## Slide 32
„Normal Anatomy“

## Slide 33
„Normal Anatomy“

## Slide 34
„Normal Anatomy“

## Slide 35
„Normal Anatomy“

## Slide 36
„Normal Anatomy“

## Slide 37
„Normal Anatomy“

## Slide 38
„Normal Anatomy“

## Slide 39
Pathologies of the
thorax /abdomen

## Slide 40: aa
Aortic Aneurysm
Notes: Klumpp, friederike *19.3.43
nicht einheitlich, meist ab 4 cm Durchmesser

## Slide 41
Perikardial
Effusion

## Slide 42
Perikardial
Effusion

## Slide 44
Liver Cysts

## Slide 45
Liver Metastases

## Slide 46
Summary
Recommended systematic imaging analysis :
Knowledge of the crucial anatomy
Imaging techniques (which contrast media? Oral/rectal contrast?)
Which imaging modality is most useful and when?

## Slide 47
Thank you for your attention!