## Slide 1: Image Analysis
Jonathan Disselhorst, PhD
Jonathan.Disselhorst@med.uni-tuebingen.de

## Slide 2: Overview
Introduction
Image Filtering
Image Segmentation
Clustering
Practical

## Slide 3: Sampling and Quantization
Digitization requires:
  Sampling (division in a grid (pixels) equally space
  Quantization (the signal is assigned to a finite set of discrete values)

## Slide 4: Computer storage
Number of discrete values depends on the number of bits available for storage, e.g.,
  1 bit: 2 numbers (0 and 1)
  2 bit: 4 numbers (00 [0], 01 [1], 10 [2], and 11 [3])
  8 bit: 256 numbers
  12 bit: 4096 numbers
  General: 2n numbers
Higher bitdepth  lower quantization error, but larger image file. Also physical sensors in imaging systems have a limited resolving power.

## Slide 5: Bit depth
3 bit
4 bit
5 bit
6 bit
7 bit
8 bit
False
contouring

## Slide 6: Resolution
Spatial resolution
  In discrete digital images, each pixel (2D) or voxel (3D) has specific dimensions in the measurement space of the object
  The limits to spatial resolution in the final image are the smallest dimensions of the object differentiable by the total imaging system, including image reconstruction
  Depends on the size of the pixels and the spatial resolution of the imaging system.
  The resolution and dimensions may differ for each orthogonal direction represented in a volume image (anisotropic) or they may be equal (isotropic)

## Slide 7: Spatial resolution: Pixel size

## Slide 8: Spatial resolution: PSF
Point spread function
  The image that results from a point object
  In many systems the PSF is approximated with a Gaussian
  Its width relates to the smallest observable detail
  … often expressed as the Full Width at Half Maximum (FWHM)
  Can be anisotropic
  The image of a complex object can be seen as a convolution of the true object and the PSF.
Anisotropic Gaussian 2D PSF
Image source: svi.nl/ & PaulBourke.net

## Slide 9: PSF: Example in 1D
FWHM << Distance between points: Points can be easily distinguished
FWHM < Distance between points: Points can still be distinguished
FWHM = Distance between points: Points can barely be distinguished
FWHM > Distance between points: Points can no longer be distinguished

## Slide 10: Partial Volume Effect
Soret et al. J Nucl Med. 2007;48:932–45.

## Slide 11: PVE: Spill-out and spill-in
Multiple effects
  Finite resolution
  Image sampling
Signal spills to other regions, spill-out and spill-in
PVE does not cause a loss, only a displacement of signal
Dependent on background
  Regions with a higher signal intensity than their surroundings appear less intense than they are
  Regions with a lower signal intensity than their surroundings appear more intense than they are
No PVE in ex vivo biodistribution studies in γ-counter
Soret et al. J Nucl Med. 2007;48:932–45.

## Slide 12: PVE: Size dependent
Smaller object: larger underestimation of signal
Larger FWHM of system, small objects appear:
  Larger
  Less active*
Recovery Coefficient shows the recovered activity in an object, related to the true activity
* When the object has a higher activity than the background
Soret et al. J Nucl Med. 2007;48:932–45.

## Slide 13: PVE. Reconstruction
In PET, the PVE also depends on the reconstruction algorithm, and the reconstruction settings.
More iterations initially decrease the FWHM
Too many iterations only increase noise.
Soret et al. J Nucl Med. 2007;48:932–45.

## Slide 14: Histograms
Not possible
Image: Dougherty (see further reading)

## Slide 15: Dynamic Range
Images: Astopix.com

## Slide 16: Histogram stretch
Images: Ogorzałek et al. DOI: 10.5772/23388 and wikipedia

## Slide 17: Histogram equalization
Histogram (in red), and the cumulative histogram (black)
Equalization creates a linear cumulative histogram
Attempts to have each pixel value appear equally frequent
No new information, hence empty bins

## Slide 18: Spatial Filtering
Image enhancement can
  Improve appearance to human viewers
  Enhance performance of computer-aided analysis/diagnosis
In the spatial domain:
  Local operations Output pixel value depends only on its corresponding input pixel value, e.g., averaging multiple acquisitions
  Neighborhood operations Output pixel value depends on the neighborhood of the input pixel

## Slide 19: Noise
Random variation of pixel intensity
Many sources and types of noise
  Gaussian noise (e.g., thermal noise)
  Periodic noise (e.g., caused by interference)
  Salt-and-pepper noise (‘dead pixels’)
  Quantum / shot noise (fluctuations in number of photons measured)
  Quantization noise
  …

## Slide 20: Convolution based operations
Image: Dougherty / Gonzalez (see further reading)

## Slide 21: Smoothing mask

## Slide 22: Gaussian Blur

## Slide 23: Sharpening
Cornsweet illusion
Images: wikipedia

## Slide 24: Frequency Filtering
 Discrete Fourier transform 
 Inverse discrete Fourier transform 
Discrete form of the Fourier transform (DFT)
Often implemented as the fast Fourier transform (FFT)
Formulas above are in 1D, for 2D the transform can be performed as two consecutive transforms in rows and cols

## Slide 25: Low Pass Filter
‘brick-wall’
Ringing artifact
Butterworth
No ringing
Image
Fourier

## Slide 26: Butterworth low pass filter
Butterworth low pass filter:
k: frequency
k0: cut-off frequency
n: order (no ringing at order 1, more ringing at higher order)

## Slide 27: Low Pass Filter

## Slide 28: Low Pass Filter

## Slide 29: High pass filter
Butterworth high pass filter:
k: frequency
k0: cut-off frequency
n: order

## Slide 30: Band pass / Band reject filter
Band pass filters are a combination of a low- and high-pass filter.
They attenuate all frequencies below a certain threshold, and above another threshold
The opposite of this is the band reject filter.
A narrow band reject filter is called notch filter
  Useful to remove noise of certain frequency.

## Slide 31: Band-Reject Filter Example

## Slide 32: Example
Fourier
Reject
Masked Fourier

## Slide 33: Example

## Slide 34: Filtering
Often equivalent results can be obtained in the spatial and in the frequency domain
Convolution in one domain is equivalent to multiplication in the other.
Large convolution kernels require a lot of computing power  frequency filtering may be advantageous
No (easy) equivalent for some operations:
  Non-linear spatial filters (e.g., median filtering)
  Band reject in frequency domain

## Slide 35: Segmentation
Segmentation into connected, homogeneous regions
  Not always easy…
  Many, many different techniques
Homogeneous
Same (similar) brightness?
Color?
Texture?
Motion?
…?
Connected regions?

## Slide 36: Manual segmentation
Interactive delineation of the boundaries of a structure
Can be accurate if an expert is doing the work
Seen as the gold standard for segmentation
Can be performed on a different modality
  E.g., analysis of PET with region from CT
Many drawbacks:
  Time consuming
  Error prone (e.g., fatigue, using a mouse for drawing)
  Biased (who is performing the segmentation?)
  Bad reproducibility (intra- and inter-observer variability)
Manual tumor size measurement, depends on window settings

## Slide 37: Fixed Volume
Not really a segmentation method
Still often used in image analysis
Examples:
  the voxel with the highest signal intensity
  group of voxels with highest mean signal intensity
  Sphere of a certain radius, e.g., 15 mm
  …

## Slide 38: Thresholding
The most widely used PET segmentation method
Very easy to perform
  A gray scale range is chosen that represents the object of interest. Voxels that are within the gray scale are set to one, all other voxels are set to zero
Different methods:
  Absolute Threshold (e.g., SUV > 4, or 2000 < HU <= 3000)
  Relative Threshold (e.g., 50% of the maximum value)
  Adaptive Threshold (Threshold level depends on aspects such as object size and scanner PSF)

## Slide 39: Absolute Thresholding
Can be set at a predefined value, e.g., SUV 2.5
The image histogram can be used to select the threshold
Image: National Instruments

## Slide 40: Relative Thresholding (I)
The threshold level is relative to a pixel value
  e.g., the maximum in the image
Affected by PVE
Affected by background
Affected by object heterogeneity
Sensitive to noise

## Slide 41: Relative Thresholding (II)

## Slide 42: Connected component analysis
Thresholding produces a binary segmentation
Sometimes multiple objects are detected
 give a different label to each of them
Separate if not connected by foreground pixels
Image
Thresholded
Binary
CCA
4-connectivity
CCA
8-connectivity

## Slide 43: Edge detection
Edges in images can be detected after:
  Optional denoising
  A gradient operation, e.g., using a Sobel operator.
  Thresholding the gradient magnitudes
  Post-processing (linking edges, etc)

## Slide 44: Morphological filters
Why?

## Slide 45: Morphological filters
Objective: Spread out and Shrink image regions
  Why?
    Fill up cavities, smooth boundaries.
    Remove small regions—probably created by noise.
    Extract edges
Albrecht Dürer, 1515

## Slide 46: Morphological Filters
Dilation
Erosion

## Slide 47: Morphological Filters
Structuring element:
Dot = 1, empty = 0
1. Point of reference.
2. Does not have to be located at the center.

## Slide 48: Morphological Filters
Dilation
H being replicated at each pixel in the image

## Slide 49: Morphological Filters
Erosion

## Slide 50: Morphological Filters
Design of a filter: Depends on what we want

## Slide 51: Morphological Filters
Different structuring elements

## Slide 52: Clustering
What is clustering?
  Grouping similar objects in to sets
  Can be seen as unsupervised classification
  Appropriate when a priori knowledge is absent
  Clustering can be performed on any data

## Slide 53: Clustering
 | 1 | 2 | … | n
1 |  |  | … | 
2 |  |  | … | 
… | … | … | … | …
m |  |  | … | 
Observations
Features
Observations are the ‘objects’ we want to group.
  In imaging: every pixel
Features are the measured parameters
  In imaging: e.g., red, green, blue in a color image, or different time points in a 4D dataset

## Slide 54: Clustering
Inter-cluster distances are maximized
Intra-cluster distances are minimized
Image: Andrei Pandre

## Slide 55: k-Means Clustering
What is ‘k’?
  The required / expected number of clusters
Can be ambiguous!
Image: Andrei Pandre

## Slide 56: k-Means Clustering
Original data:
2 features (x,y)
k=2 Clusters?
Choose (random) centroid for clusters
2. Assign points to closest centroid
3. Recalculate centroids of all clusters
4. Repeat step 2 and 3
Until convergence
Final clustering
Image: Chris Piech, Stanford University

## Slide 57: Clustering example

## Slide 58: Principal component analysis (PCA)
Principal Component Analysis (PCA) aims to transform a number of possibly correlated variables into a smaller number of uncorrelated variables called principal components.
The set of reduced variables can be used for data mining, interpretation and visualization.

## Slide 59: PCA
x1
x2
Low redundancy
High redundancy
x1
x2
x1
x2
Figure adapted from “a tutorial on principal component analysis“, Jon Shlens
Notes: A spectrum of possible redundancies in data from the two separate measurements x1 and x2

## Slide 60: PCA example — RGB image
Original image
R component
B component
G component

## Slide 61: PCA example — RGB image
PC-1 (92.7%)
PC-2 (6.3%)
PC-3 (1%)
Original image
Gray scale image
Reconstructed
PC-1 (92.7%)
Reconstructed
PC-1-2 (99%)
Reconstructed
PC-1-3 (100%)
0.6R
0.6G
0.5B
-0.6R
-0.1G
0.8B
-0.5R
0.8G
-0.3B

## Slide 62: Further reading
Geoff Dougherty Digital Image Processing for Medical Applications
Rafael Gonzalez & Richard Woods Digital Image Processing

## Slide 63: Practical
jonathan.disselhorst.eu/imageanalysis